## Slide 1: Comprehensive VHDL Hamdi Abdelbagi Phone: (937) 830-7761 Email: abdelbagih1@udayton.edu

## Slide 2: Introduction
Aim
  To obtain general appreciation of what VHDL is, and how it is used in design process
Topics covered
  What is VHDL?
  History of VHDL
  VHDL design flow and tools
  SRAM-based FPGAs
  Benefits of VHDL
  VHDL resources

## Slide 3: What is VHDL
VHDL is VHSIC Hardware Description Language
VHSIC = Very High Speed integrated Circuit
IEEE standard 1076, defined by Language Reference Manual
  All rights were given away be the DoD to the IEEE
1987 Publication of IEEE Standard 1076-1987
1994 - Revised standard , VHDL 1076-1993
2000 – Revised edition incorporating
2002 – Revised edition incorporating 1076-2000 plus buffer port changes
  To use VHDL at all, you need to learn the language; but to use VHDL effectively you need to learn how tools especially synthesis too interpret your VHDL.
Effective VHDL = Know VHDL + Know how tools interpret VHDL

## Slide 4: Design Flow
Design Entry (Design RTL, testbench)
Simulation(verification, debugging)
Synthesis/Fitting(Deign, no TB)
Hardware (bitstream, mask)

## Slide 5: Tools
Design Capture:
  Text editor, graphical entry, SM entry…
Simulator:
  Simulation testbench (non-synthesisable) and design (synthesisable) to verify fictional correctness.
Synthesis Tool:
  Translate synthesisable code into gate level netlist in chosen technology
Netlist Mapping:
  R-Map gate level netlist to technology primitive cells
Place and Route:
  Place cells on chip and route wiring
Time Analysis:
  Analyze time “Static Timing Analysis”
Hardware:
  Produce masks (application-specific integrated circuit (ASIC)), bitstream (FPGA)

## Slide 6: SRAM-based FPGA

## Slide 7: SRAM-based FPGA
CLB: Configurable Logic Block

## Slide 8: SRAM-FPGAs Typical Logic Block
Typical Logic Cell can include 1,2, or up to 4 registers
Every Architecture is compromise:
  Usually allergic to very wide combinational faction
  C-logic is wasted when too many FFs are used

## Slide 9: FPGA Logic Block
The storage cells in the LUPs in an FPGA are volatile
  Losing stored contents whenever the power is off
Using PROM to hold data permanently
The storage cells are loaded automatically from PROM when the chip is initialized

## Slide 10: FPGA Extra Feature
In-system configurability
Start-up block, Oscillators
RAM/ROM/CAM-Content-addressable memory
  Dedicated and/or distributed
PLLs and Clock-related feature
Specific high speed IO standard (LVDS, GTS (Global Three State)….)
Bus interface (PCI)
Embedded microprocessor cores
ETC…

## Slide 11: Benefits of VHDL
Executable specification
    Validate specs in system contact. Subcontract
Functionality separated from implementation
simulate early and fast. Mange complexity
Explore design alternatives
get feedback. Produce better design
Automatic synthesis and test generation
Increase productivity. Shorten time to market
Protect your investment

## Slide 12: VHDL World
VHDL on the internet

## Slide 13: Getting Started
Aim
  To understand the overall flow of VHDL project
Topics covered
  entity, port and architecture
  Testbenches
  Libraries and compilation
  tool flows

## Slide 14: The Design Entity
Examples:
  Printed circuit board
  Microprocessor
  CPLD
  Counter
  AND gate

## Slide 15: Entity, Port and Architecture
Entity
A module
Port
external connections
Architecture
functionality

## Slide 16: Testbenches
Testbench
  Any entity without ports
Instantiation
  The device under test
Signals
  Wired connections
Stimulus
  Process to drive inputs

## Slide 17: Testbench

## Slide 18: Stimulus Process
Process statements execute sequentially
Sequential signal assignments schedule new value
Wait statements pause process

## Slide 19: Compilation

## Slide 20: Compilation Order
VHDL file 2 instantiates design unit from VHDL file 1
Compile VHDL file 1 into the library first

## Slide 21: Typical Functional Simulation Flow
All simulators follow these steps
Most simulators support TCL scripting
  TCL = Tool Command Language
Script automation improve productivity
  Repeatable operation
  Executable documentation
  Saves time

## Slide 22: Typical Synthesis Flow
Synthesis tool can be:
  Stand alone
  Integrated with FPGA tool suite
Common feature include:
  FSM optimization
  Resource sharing
  RTL view
  Technology view
Synthesis can be scripted

## Slide 23: Recommended Design Style for Sythesis
All storage is flip-flops with a single external clock
No combinational feedback loops

## Slide 24: Timing Constraints

## Slide 25: Typical FPGA implementation Flow
Tools are provided by FPGA vendor
Implementation can be scripted